## Slide 1: Basic Switch configuration
Will focus on basic switch configuration, interface configuration and remote access configuration

## Slide 2: Switch configuration is almost identical to router configuration.
At any point enter “?” to show all available prompts at the current location.
Config t
  Hostname #name#
  Banner motd # something #
Line con 0
Login
Password #anything#
Logging sync
Line aux 0
Login
Password #anything#
Logging sync
  Exit
Enable secret #anything#
Service password-encryption
Ip domain-name #anything#
Username #name# secret #password#
Crypto key generate rsa general keys (crypto key generate rsa ?)
1024
Ip ssh version 2
Line vty 0 4
Login local transport input ssh
Exit
Interface vlan 1
  Ip address #address# #subnetmask#
  (this allows us remote SSH access via any interface by connecting to the selected ip address. Even though the switch dose not use ip addresses unless it is a Layer 3 switch.